## Slide 1
Spin-based Neuromorphic Computing (Simulation)
Presented by: CHONG TIAN EN
Supervised by: S.N. Piramananyagam
Associate Professor
Division of PAP, SPMS
Co-supervised by: Mohamed M. Sabry
Assistant Professor
SCSE
5
th
May 2020

## Slide 2
Computing Devices
Performance gained by scaling current semiconductor technologies will hit limit within 10-15 years.
All based on von Neumann Architecture
National Research Council, Enhancing Productivity Growth in the Information Age, 91 (2007)

## Slide 3
von Neumann Architecture
Memory unit is situated very far from CPU
Frequent data transfer between CPU and Memory Unit consumes more energy and time than actual computation
D. Thompson, “Beyond Von Neumann: Moore’s Law and the Shift from Near-Memory to In-Memory Compute”, (2019)

## Slide 4
2 petaFLOPS
13MW
Processing Speed vs Power Consumption
https://www.olcf.ornl.gov/olcf-resources/compute-systems/summit/
100 1000 petaFLOPS
15W (when solving a physics problem)
“Brains greatly exceed digital computers in computation per volume per watt”, http://webhome.phy.duke.edu/~hsg/414/images/brain-vs-computer.html
more performance
less power

## Slide 5
Introduction
Biological Neural Network
Artificial Neural Network
Notes: Mimic human brain neuron and synapse network
Scope of project: not micromagnetic, but electronic neuromorphic circuit simulation

## Slide 6
Artificial Neural Network
Huge application in AI Computer Vision
Introduction
Notes: Scope of project: not micromagnetic, but electronic neuromorphic circuit simulation

## Slide 7
Artificial Neural Network
Deeper layer network can extract subtler visual details
Introduction
M. Mitchell Waldrop, PNAS January 22, 2019 116 (4) 1074-1077
Notes: Scope of project: not micromagnetic, but electronic neuromorphic circuit simulation

## Slide 8
Artificial Neural Network
Network output can be fed for efficient visual object recognition
Introduction
1
0
0
0
0
0
1
0
0
0
0
0
1
0
0
0
0
0
1
0
0
0
0
0
1
Traffic Light
Person
Handbag
Truck
Bus
Notes: Scope of project: not micromagnetic, but electronic neuromorphic circuit simulation

## Slide 9
Artificial Neural Network
Implemented in von Neumann Architecture
Introduction
Notes: Scope of project: not micromagnetic, but electronic neuromorphic circuit simulation

## Slide 10
Artificial Neural Network
Introduction
Neuromorphic Computing Circuit
Neuron Outputs
Neuron row
Adapted from: A. Sengupta and K. Roy APPLIED PHYSICS REVIEWS 4, 041105 (2017)
Notes: Scope of project: not micromagnetic, but electronic neuromorphic circuit simulation

## Slide 11
Artificial Neural Network (ANN)
Notes: Scope of project: not micromagnetic, but electronic neuromorphic circuit simulation

## Slide 12
Artificial Neural Network (ANN)
  Involves:
  Tensorflow (Machine Learning Platform)
  Keras (Python Deep Learning Library)
  OpenCV (Computer vision and machine learning library)

## Slide 13
Neuron Outputs
Neuron row
Artificial Neural Network
Introduction
Neuromorphic Computing Circuit
A neuron
Notes: Scope of project: not micromagnetic, but electronic neuromorphic circuit simulation

## Slide 14
Neuromorphic Computing Circuit
Neuromorphic Computing Circuit
Neuron Outputs
Neuron row
Use Kirchhoff’s Current Law for simultaneous summation, not von Neumann CPU that sums one by one
Operation:
Notes: Scope of project: not micromagnetic, but electronic neuromorphic circuit simulation

## Slide 15
Neuromorphic Computing Circuit
Neuromorphic Computing Circuit
Neuron Outputs
Neuron row
Use Ohm’s Law for simultaneous multiplication, not von Neumann CPU that multiplies one by one
Operation:
1
2
Notes: Scope of project: not micromagnetic, but electronic neuromorphic circuit simulation

## Slide 16
Neuromorphic Computing Circuit
Neuromorphic Computing Circuit
Neuron Outputs
Neuron row
Synapse Resistor  Spintronic domain wall device
Memory:
Notes: Scope of project: not micromagnetic, but electronic neuromorphic circuit simulation

## Slide 17
Spintronics as Memory
Involve in:
Spin Transfer Torque (STT) for reading
Spin Orbit Torque (SOT) for writing
Note:
This project only simulates electronic circuit (with MRAM 8-step resistance range), not micromagnetic scope physics.
8-step, 9-level Domain Wall MRAM
STT
SOT
Pinned Layer
A. Sengupta and K. Roy APPLIED PHYSICS REVIEWS 4, 041105 (2017)
Free Layer

## Slide 18
Spintronics as Memory
Non-volatile (information retention during power loss) like Solid State Drive (SSD) unlike Metal Oxide Semiconductor (MOS) and leaky Capacitors in DRAM
Solid State Drive (SSD)
Computer DRAM Module and Circuit Diagram
“DRAM Operation: how does dynamic RAM work”, electronic-notes

## Slide 19
Spintronics as Memory
Similar to SSD, Magnetic Tunnel Junction (MTJ) uses electron tunnelling (through MgO Layer)
But, MTJ uses electron spin orientation ( instead of electron presence in SSD (charge retention changes threshold voltage, causing wear out)
Some charge stuck here even after wiping
Jacquelyn, The physical structure of flash memory, ELINFOR (2018)

## Slide 20
Spintronics Memory Advantage vs Conventional SSD
Higher read/write speed
Lower power
Data does not degrade overtime
J. Arulraj et al., “Let’s Talk About Storage & Recovery Methods for Non-Volatile Memory Database Systems ”
MRAM () and SSD ():
S. A. Wolf et al., "The Promise of Nanomagnetics and Spintronics for Future Logic and Universal Memory,“, Proceedings of the IEEE, 98 (12), 2155-2168 (2010).

## Slide 21
Neuromorphic Computing Circuit
Neuromorphic Computing Circuit
Neuron Outputs
Neuron row
In short:
Hardware based implementation of neural network
Application-Specific Integrated Circuit (ASIC)
Not for General Purpose Computing (Forget YouTube, Email, … etc)
Only on von Neumann Architecture
Notes: Scope of project: not micromagnetic, but electronic neuromorphic circuit simulation

## Slide 22
Objective
To create and simulate model of practical, manufacturable (non-ideal) neuromorphic network, incorporated with 8-step domain wall MRAM resistance range based synapses
To compare the performance between traditional software (Tensorflow) implemented neural network (ANN) and (Cadence) neuromorphic model .
Neuron Outputs
Neuron row
VS
ANN in TensorFlow
Neuromorphic in Cadence

## Slide 23
Simulation Details (Outline)
Theory:
  Inverting Summing Operational Amplifier (OpAmp)
  Synaptic Weight
  Weight→Resistance
  Matrix Implementation
Actual Simulation Environment:
  Cadence Development Environment with 65nm Process Design Kit (PDK)
  Code Files
  Programmable Scalable Network (Generated)

## Slide 24
Inverting Summing OpAmp
Note & should be:
As high as possible to reduce power consumption
Scale with number of incoming source
Too low & cause the ideal relationship above break down due to non-zero virtual ground voltage
Ideally,
0V

## Slide 25
Tuned 741 Texas Instrument OpAmp Model

## Slide 26
Synaptic Weight
Note:
means weight from node to node
m = 4
n = 3

## Slide 27
Weight Resistance

## Slide 28
Matrix Implementation

## Slide 29
Cadence Development Environment with 65nm PDK

## Slide 30
Code Files
SKILL file (generates scalable circuit design) – scaled.il
OCEAN file (automates simulation process) – vlsim.ocn
PYTHON file (generates data files v_arr & r_arr) – initvar.py
Data files
  v_arr (set )
  r_arr (set )
  sumVlsiSetup (set values)

## Slide 31
4 by 4 synapses
4 neurons
Programmable Scalable Network (Generated)
m
n
m
n

## Slide 32
Programmable Scalable Network (Generated)
40 by 40 synapses, 40 neurons

## Slide 33
Pre-Simulation Result (Outline)
Choice of switch (NMOS? PMOS?)
20 by n synapses without switch to find (All same )
20 by 784 synapses with switch & synapses (8-step 1k to 3k) and all different (1326000, 50000, 281690) to tune accuracy for:
  Normal power case
  Extreme power case

## Slide 34
Choice of MOS switch (NMOS? PMOS?)
Closeness (simulated/ideal in %) | 80.305877
S.D. (%) | 3.034855
NMOS

For , , :
Closeness (simulated/ideal in %) | 67.714079
S.D. (%) | 3.941705
PMOS

## Slide 35
20 by n synapses without switches (determine )
Note:
Good value means close to 100% with low error.
here means .

## Slide 36
20 by 784 Synapses with switch & 8-step R (Normal)

## Slide 37
20 by 784 Synapses with switch & 8-step R (Ex)
Simulated (V) | Ideal (V)
2.766582 | 4.973581
(simulated/ideal in %) | 55.625561
Simulated (V) | Ideal (V)
2.766582 | 4.973581
 | 55.625561
Simulated (V) | Ideal (V)
2.653436 | 1.617143
(simulated/ideal in %) | 164.081739
Simulated (V) | Ideal (V)
2.653436 | 1.617143
 | 164.081739
(All low R, high power consumption), same , same random
(All high R, low power consumption), same , same random
Pinned Layer
Pinned Layer
Free Layer
Free Layer
All R = 1000
All R = 3000
Notes: Nebi Caka
Professor at University of Prishtina, Faculty of Electrical and Computer Engineering
In a semiconductor the mobility of electrons (referring to ‘conduction electrons’ or ‘free-electrons’) is greater than that of a holes (indirectly referring to ‘valence electrons’) because of different band structure and scattering mechanisms of these two carrier types.
Conduction electrons (free-electrons) travel in the conduction band and valence electrons (holes) travel in the valence band. In an applied electric field, valence electrons cannot move as freely as the free electrons because their movement is restricted. The mobility of a particle in a semiconductor is larger if its effective mass is smaller and the time between scattering events is larger.
Holes are created by the elevation of electrons from innermost shells to higher shells or shells with higher energy levels. Since holes are subjected to the stronger atomic force pulled by the nucleus than the electrons residing in the higher shells or farther shells, holes have a lower mobility.
In an intrinsic silicon, at temperature 300 K:
Electron mobility = 1500 cm2/(V∙s)
Hole mobility = 475 cm2/(V∙s)

## Slide 38
Case Study - MNIST
  MNIST (Standard Handwritten Digit Dataset)

## Slide 39
MNIST General Simulation Steps (Outline)
Explore ANN architectural layer types
Discover ANN Weights and MRAM Resistance Relationship
Explore weight processing function to maintain previous relationship
Train different MNIST architectures/model (pick best one and transfer to neuromorphic circuit, … and voila!)

## Slide 40
MNIST ANN Preliminary Simulation Result
Input -> FCN 100 -> output
Accuracy : 11.78%
Input -> FCN 100 (ReLU) -> output
Accuracy : 11.35%
Input -> FCN 100 (ReLU) -> output (ReLU)
Accuracy : 9.80%
Input -> FCN 100 (ReLU) -> output (Softmax)
Accuracy : 96.91%
Input -> FCN 100 (Softmax) -> output (Softmax)
Accuracy : 54.97%
Output
Output
Input
Input

## Slide 41
ANN Architecture Layer Introduction
1 Convolution Layer (1 Conv)
1 Maxpooling Layer (Maxpool)
5 Fully Connected Layer (5 FCN)
1
2
3
4
5
“Starting with convolutional neural network (CNN)”, datascienceplus (2019)
“Deep Convolutional Neural Networks an Introduction”, mbenhaddou.com (2019)

## Slide 42
ANN Weight and MRAM Resistance Relationship
Physical R () | R (Ω) | Comp. w | Decomp. w
1000 | 1.0 | 1.0 | 1.0
1250 | 1.25 | 0.8 | 0.7000
1500 | 1.5 | 0.6667 | 0.4999
1750 | 1.75 | 0.5714 | 0.3571
2000 | 2.0 | 0.5 | 0.25
2250 | 2.25 | 0.4444 | 0.1667
2500 | 2.5 | 0.4 | 0.1000
2750 | 2.75 | 0.3636 | 0.0454
3000 | 3.0 | 0.3333 | 0
 | R (Ω) | Comp. w | Decomp. w
1000 | 1.0 | 1.0 | 1.0
1250 | 1.25 | 0.8 | 0.7000
1500 | 1.5 | 0.6667 | 0.4999
1750 | 1.75 | 0.5714 | 0.3571
2000 | 2.0 | 0.5 | 0.25
2250 | 2.25 | 0.4444 | 0.1667
2500 | 2.5 | 0.4 | 0.1000
2750 | 2.75 | 0.3636 | 0.0454
3000 | 3.0 | 0.3333 | 0
TensorFlow weight constraint

## Slide 43
ANN Weight Processing - CompDecomp
    ComDecomp - MRAM non uniform 8-step rounding, lossless compression and decompression (no weight clipping at boundaries)

## Slide 44
ANN Weight Processing - Limit
    Limit - Continuous scaling (lossy weight clipping at boundaries)

## Slide 45
ANN Weight Processing - StepUniform
    StepUniform - Uniform n-step scaling (cf. MRAM non-uniform 8-step scaling)

## Slide 46
Unprocessed Accuracy
20 FCN
1000 FCN
20 Conv Maxpool 10 FCN
100 Conv Maxpool 10 FCN
(20 Conv Maxpool)2 10 FCN
90.20%
92.52%
95.61%
96.27%
97.97%
20 Conv Maxpool 50 Conv Maxpool 10 FCN
98.14%

## Slide 47
CompDecomp Accuracy
20 FCN
1000 FCN
20 Conv Maxpool 10 FCN
100 Conv Maxpool 10 FCN
(20 Conv Maxpool)2 10 FCN
20 Conv Maxpool 50 Conv Maxpool 10 FCN
80.24%

## Slide 48
Limit Accuracy
20 FCN
1000 FCN
20 Conv Maxpool 10 FCN
100 Conv Maxpool 10 FCN
(20 Conv Maxpool)2 10 FCN
20 Conv Maxpool 50 Conv Maxpool 10 FCN

## Slide 49
StepUniform Accuracy
)
20 FCN
1000 FCN
20 Conv Maxpool 10 FCN
100 Conv Maxpool 10 FCN
(20 Conv Maxpool)2 10 FCN
20 Conv Maxpool 50 Conv Maxpool 10 FCN

## Slide 50
MNIST Neuromorphic Circuit Architecture
FCN Layer
20×784 FCN Layer
FCN Layer
10×20 FCN Layer
Input
Final Output
Intermediate Output
Input
Final Output
Intermediate Output

## Slide 51
Simulation Result (20 by 784 Single Stage Summing)
S.D. = 53.8% (after scaling average to 100%)
Average Closeness (%) | 101.02436
S.D. (%) | 54.367929

## Slide 52
Simulation Result (20 by 784 Double Stage Summing)
S.D. = 54.0% (after scaling average to 100%)
Average Closeness (%) | 17.794647
S.D. (%) | 9.602465

## Slide 53
MNIST Neuromorphic Circuit Architecture
FCN Layer
20×784 FCN Layer
FCN Layer
10×20 FCN Layer
Input
Final Output
Intermediate Output
Input
Final Output
Intermediate Output

## Slide 54
MNIST 10 20 FCN Neuromorphic Layer
Neuron outputs are measured and Softmax function is applied (not implemented in circuit)

## Slide 55
MNIST 10 20 FCN Neuromorphic Layer
Location of maximum value is extracted to predict the 10000 MNIST test dataset samples
0.1000 | 0.0981 | 0.0994 | 0.1002 | 0.1000 | 0.0995 | 0.0994 | 0.1029 | 0.0992 | 0.1011
[0] | [1] | [2] | [3] | [4] | [5] | [6] | [7] | [8] | [9]

## Slide 56
MNIST Simulation Result (MNIST 10 20 FCN)
Accuracy | 81.02%
vs 80.24% (Tensorflow) (Surprisingly better with circuit errors!)

## Slide 57
Discussion
Need to retune with network of different scale to obtain high closeness (simulated/ideal value in %).
Deeper layer networks bring high ideal accuracy in Tensorflow, but low accuracy for neuromorphic circuit (more errors resulted).
20 Conv Maxpool 50 Conv Maxpool 10 FCN
98.14%
20 Conv Maxpool 50 Conv Maxpool 10 FCN (CompDecomp)
9.8%
Notes: we need to strike a balance.
MRAM limited 8 steps weights rounding result in reduced accuracy due to not representing weights faithfully, which can be solved with higher steps weight representation.

## Slide 58
Discussion
0V
Need to scale to amplify simulated value to ideal value (virtual ground no longer 0V).

## Slide 59
Discussion
0V
Larger network cause OpAmp virtual ground voltage to stuck at high voltage (ideal equation breaks).

## Slide 60
Conclusion
Neuromorphic computing offers high accuracy for off-chip training TensorFlow architecture
Suffers scaling issues due to non-ideal OpAmp behaviour and MRAM limited 8-step weight representation
81.02% for MNIST 10 × 20 FCN

## Slide 61
Future Work
Sourcing a higher precision opamp
Creating an opamp that can sustain 0V virtual ground voltage.
Re-simulating large scale end-to-end neuromorphic circuit after overcoming OpAmp limitation.
Implementing and simulating micromagnetic scope domain wall synapse based neuromorphic circuit.

## Slide 62
Future Work
Exploring spiked based neural network and its neuromorphic equivalent

## Slide 63
Thank you!