## Slide 1: Spin-based Neuromorphic Computing (Simulation)
Chong Tian En

## Slide 2: Neuromorphic Computing
Hardware based implementation of neural network
Application-Specific Integrated Circuit (ASIC)
Not for General Purpose Computing (Forget YouTube, Email, … etc)

## Slide 3: Neural Network

## Slide 4: Why Neuromorphic Computing?
Huge application in AI Computer Vision
Mimic human brain neuron and synapse network
Very efficient for visual object recognition
Low power consumption
Deeper layer network can extract subtler visual details
Network output can be fed for image classification

## Slide 8: IBM TrueNorth Chip
4096 cores
256 neurons/core
256 synapses/neuron
Only consumes 63mW
"Neuromorphic Hardware: Trying To Put Brain Into Chips." Medium. N.p., 2019. Web. 18 Dec. 2019.

## Slide 9
Power Density of Conventional
von Neumann Processor
"Neuromorphic Hardware: Trying To Put Brain Into Chips." Medium. N.p., 2019. Web. 18 Dec. 2019.

## Slide 10: Neural Network
synapses in 1st layer
1 step needed
synapses 1 step

## Slide 11: von Neumann Processor
synapses in 1st layer
10 steps needed
Synapses steps

## Slide 12: Motivation (Use of Spintronics)

## Slide 13: Why Spin-based (Spintronics)?
Originally used in hard disk drive read/write head
Involve in:
Spin Transfer Torque(STT)
Spin Orbit Transfer (SOT)
Tunneling Magnetoresistance (TMR)
Giant Magnetoresistance (GMR)
for magnetoresistive application like Magnetoresistive Random-access Memory (MRAM)

## Slide 14: Why Spin-based (Spintronics)?
Non-volatile (information retention during power loss) like Solid State Drive (SSD) unlike Metal Oxide Semiconductor (MOS) and Capacitors
Similar to SSD, MTJ uses electron tunnelling
MTJ has smaller footprint to CMOS (Main reason)
But, MTJ uses electron spin orientation instead of electron presence in SSD (charge retention changes threshold voltage, causing wear out)

## Slide 15: MTJ Memory Cell (Old model as Ilustration)

## Slide 16: MOSFET (PMOS and NMOS)

## Slide 17: MOSFET IV Characteristics

## Slide 18: SSD Nand Flash

## Slide 19: Spintronics Advantage vs Conventional SSD
Higher read/write speed
Lower power
No wear out (Unlimited read/write cycle)
"What is MRAM Memory Technology" Medium. N.p., 2019. Web. 18 Dec. 2019.

## Slide 20: Simulation details

## Slide 21: E.g. 3 by 4 Matrix

## Slide 22: Weight (Continued)
Note:
means weight from node to node

## Slide 23: Theoretically and Ideally…
Note:
Matrix in m by n dimension

## Slide 24: Practically and Physically …
Relate weight to resistance
No physics for , only for
Hence, , or simply,

## Slide 25: Weight Resistance

## Slide 26: Matrix Operation
Is that all for circuit design? Not so simple!
Where

## Slide 27: Inverting Summing OpAmp
Note:
& should be as high as possible to reduce power consumption
Too high & cause the ideal relationship above break down
& should scale with number of incoming source
Ideally,

## Slide 28: Practical OpAmp Limitation
OpAmp limited by
number of means each need to scale down to
Limited output gain (practical) vs infinite (ideal)
Finite input resistance (practical) vs Infinite input resistance so no current flow in (ideal)
Finite output resistance (practical) vs 0 output resistance (ideal)

## Slide 29: Matrix Operation (modified)

## Slide 30: Matrix Operation (modified)
Look redundant in math? This is a must in circuit implementation!

## Slide 31
65nm Process Design Kit

## Slide 32: Cadence Development Environment

## Slide 33: 741 OpAmp Model

## Slide 34
3 by 4 synapses
4 neurons
Note:
Matrix in n by m dimension due to diagonal flipping

## Slide 35
40 by 40 synapses
40 neurons

## Slide 36: Code Files
SKILL file (for coding scalable schematic design) – scaled.il
OCEAN file (for coding auto test flow) – vlsim.ocn
PYTHON file (V and R test values generation to data files v_arr & r_arr) – initvar.py
Data files
v_arr (set )
r_arr (set )
sumVlsiSetup (set values)

## Slide 37
scaled.il
vlsim.ocn
initvar.py

## Slide 38: Results

## Slide 39
Simulated Calculated Closeness in %
0.565875 0.580128 97.543117
2.782740 2.858339 97.355158
2.505678 2.538183 98.719345
2.080225 2.096747 99.212025
Reference (with Closeness 100%)
, n = 3, m = 4

## Slide 40
Simulated Calculated Closeness in %
3.382832 3.455852 97.887077
2.492031 2.514025 99.125146
2.050317 2.056614 99.693787
4.055174 4.152284 97.661288
1.997813 2.010950 99.346700
2.287353 2.307829 99.112730
1.711722 1.723161 99.336167
2.314272 2.342073 98.812965
1.607062 1.608447 99.913893
2.818629 2.866287 98.337294
3.855918 3.950264 97.611663
1.690216 1.683556 100.395546
0.647803 0.625310 103.596977
3.007529 3.061375 98.241130
2.609220 2.641702 98.770396
1.731220 1.735840 99.733862
0.967000 0.948559 101.944104
2.770710 2.808790 98.644242
3.414040 3.480872 98.080017
2.507560 2.530245 99.103453
Same , same n, m = 20 (increase no. of columns)

## Slide 41
Simulated Calculated Closeness in %
2.407520 2.786503 86.399331
3.148906 3.764218 83.653647
2.389537 2.752610 86.809858
2.271663 2.651160 85.685643
Same , n = 20 (increase no. of rows), same m

## Slide 42
Same , n = 40 (increase no. of rows), same m
Simulated Calculated Closeness in %
1.414525 2.182415 64.814665
1.351934 2.086400 64.797425
1.360665 2.030461 67.012634
1.474293 2.237327 65.895287

## Slide 43
Simulated Calculated Closeness in %
2.461681 2.514250 97.909155
2.296731 2.346236 97.890015
1.903122 1.877480 101.365788
1.617127 1.650176 97.997250
New Reference (Scaled Up with Closeness 100%)
, n = 20 (increase no. of rows), m = 4

## Slide 44
Simulated Calculated Closeness in %
3.208478 2.740139 117.091776
2.595280 2.244113 115.648334
1.339105 1.128274 118.686145
3.210356 2.737751 117.262518
Same , n = 3 (reduce no. of rows), m = 4

## Slide 45: MOSFET Experimentation

## Slide 46: Programmable Scalable Network

## Slide 47: Discussion

## Slide 48: Ideally, what do we want?
Infinite circuit scaling
Means 100% matched values with 0 error or standard deviation

## Slide 49: Based on Previous Result, What’s Wrong?
Ocean Script Bug ( stuck at 50000. Remember those % exceeds 100%? Very hard to discover, but easy to solve.)
Very Non-ideal OpAmp (Actual TI 741 vs Cadence Implemention with 65nm PDK. Discovered from the beginning, spent weeks to solve, it turns out not so hard afterall with “thinking out of the box”.)
Noise increases when increases, so with the number of . OpAmp also amplifies the noise (Noise shouldn’t matter since we are not doing AC but just take DC stable value right? Wrong! We need small timeframe, think nanoseconds, DC hasn’t reached its stable value yet!)

## Slide 50: Ideal OpAmp (Just what we need to know enough to use)
Note:
(grounded) for easy understanding.

## Slide 51: TI OpAmp 741 Package

## Slide 52: TI OpAmp 741 Schematic

## Slide 53: Offset Null Tuning
Basically, we can add resistor with appropriate resistance in parallel with those 2 resistors.
So that

## Slide 54: What so difficult to tune then?
No number of resistance added in parallel can change the close to 0 significantly.
Due to the relationship:

## Slide 55: Effective Resistance Graph ()
Note:

## Slide 56: What to do then?
Simple, just tune one of the resistor until we reaches
And it works! Previously, our measurement starts to go hay wire when (I am not showing you those rubbish results), the graph later will show how far we have come with extended range and lower error.

## Slide 58: Circuit scaling and [Old Assumption]
No more or less. Must be just right.
Due to power consumption? Non-ideal effect?

## Slide 59: Circuit scaling and
Note:
Good value means close to 100% with low error.
here means .
Model xycube3 (User)
Equation a*(x^3)*(y^3)+b*(x^3)*(y^2)+c*(x^3)*y+d*(x^3)+e*(x^2)*(y^3)+f*(x^2)*(y^2)+g*(x^2)*y+h*(x^2)+i*x*(y^3)+j*x*(y^2)+k*x*y+l*x+m*(y^3)+n*(y^2)+o*y+p
Reduced Chi-Sqr 714.846761334228
Adj. R-Square 0.88555125529964
Value Standard Error
Percentage a -3.40118964147559E-23 4.44279966677437E-22
Percentage b -3.3808777225304E-17 8.2557808192898E-16
Percentage c -2.0259689587371E-12 3.61725948885066E-10
Percentage d 3.05421829039265E-7 3.11204579295629E-5
Percentage e 1.92465908629804E-20 1.64731730408421E-19
Percentage f -1.55450903885609E-14 3.06407421899329E-13
Percentage g 1.13182576777577E-8 1.34640724225518E-7
Percentage h -3.85131129416287E-4 0.0114965996521702
Percentage i -1.48264432713436E-18 1.4260049552801E-17
Percentage j 1.33599679889964E-12 2.65612549419855E-11
Percentage k -1.4137600682012E-7 1.1725381816539E-5
Percentage l -0.260480613981356 0.989939319105463
Percentage m 5.92946586687354E-17 2.14080692056229E-16
Percentage n -9.87499996805226E-11 3.98894294313358E-10
Percentage o 4.46259065749002E-5 1.76439168641693E-4
Percentage p 93.4097157841867 14.8960306390529

## Slide 60: Issues to be Resolved [Old]
Higher value of needed for larger scale summing amplifier
value that is too high can overshoot the computed V value and vice versa
For m = 1,
Power
To maintain the same power consumption after scaling,
Power

## Slide 61: Issues to be Resolved
Get 65nm PDK mosfet model to work (Strong gate current? Drain voltage 0 -> open circuit, mosfet not turning on?
Need mosfet to be used as a switch (not so ideal after all? These mosfet only add more noise and screw up our result further with lower scalability) to isolate resistors to program them individually

## Slide 63: Planned Roadmap (subjected to change)
Develop a Single Simplified Spike-based Neuron Model
Spike-based Neuron Model Scaling
Implement Spintronic MRAM
MNIST Data Simulation & Comparison
Spike-based MNIST Data Simulation & Comparison